## Slide 1: Industrial Pharmacy II Assist. Lect. Amenah M. M.

## Slide 2: Tablet Design and Formulation

## Slide 3: Tablet Excipients

## Slide 4: Tablet excipients must meet certain criteria in the formulation. 1. They must be nontoxic. 2. They must be commercially available. 3. Their cost must be acceptably low. 4. They must not be contraindicated by themselves (e.g ., sucrose) or because of a component (e.g ., sodium) in any segment of the population.

## Slide 5: 5. They must be physiologically inert. 6. They must be physically and chemically stable. 7. They must be free of any unacceptable microbiologic load. 8. They must be color-compatible

## Slide 6: 9. If the drug product is also classified as a food, (certain vitamin products), the diluent and other excipients must be approved direct food additives. 10. They must have no deleterious effect on the bioavailability of the drug(s) in the product.

## Slide 7: 1. Diluents Diluents are fillers designed to make up the required bulk of the tablet when the drug dosage itself is inadequate to produce this bulk. The dose of some drugs is sufficiently high that no filler is required (e.g., aspirin and certain antibiotics). This provides a tablet weight range of perhaps 120 to 700 mg for standard density organic materials. By using oval tablets, which may be easier to swallow, tablets weighing up to 800 mg or more may be produced.

## Slide 8
Tablet formulations may contain a diluent for secondary reasons:
To provide better tablet properties such as improved cohesion.
To permit use of direct compression manufacturing, or
To promote flow.

## Slide 9
There are cited cases of pharmaceutical manufacturers actually producing products in which an excipient reduced the bioavailability of a drug, or in which chemical incompatibilities existed. The former situation occurred with the marketing of an antibiotic that utilized a calcium salt as the diluent.

## Slide 10
The tetracycline product made with a calcium phosphate filler had less than half the bioavailability of the standard product.
Divalent and trivalent cations form insoluble complexes and salts with a number of amphoteric or acid functionality antibiotics, which greatly reduces their absorption (which is also why milk should not be co-administered with these drugs).

## Slide 11
A classic case of a chemical incompatibility that went unrecognized for several years was the interaction of certain amine drugs with the commonly used diluent lactose, in the presence of a metal stearate lubricant (such as magnesium stearate); the resulting tablets were gradually discolored with time.

## Slide 12
Tablet formulators should remember that physical and chemical interactions between formulation components may be promoted by the intimate contact between potential reactants that are tightly compressed together in a tablet compact. Thus, materials that are capable of forming a eutectic mixture, for example, may pose no problem when loosely packed as a powder in a capsule in while the same formation quickly softens and becomes unacceptable.

## Slide 13
Diluents that exist In their common salt form as hydrates, containing appreciable bound water as water of crystallization, may nevertheless be excellent for very water-sensitive drugs, provided that the bound water is not released under any elevated storage condition to which the product might be exposed. Dibasic calcium phosphate and calcium sulfate have the advantages of possessing low concentrations of unbound moisture and having a low affinity for atmospheric moisture.

## Slide 14
These are required features for any excipient material to be combined with a water-sensitive drug. The bound water of calcium sulfate is not released until a temperature of approximately 80°C is reached. Such bound water is usually unavailable for chemical reaction. Such excipients containing tightly bound water but having a low remaining moisture demand may be vastly superior to an anhydrous diluent, which has a moderate to high moisture demand.

## Slide 15
Lactose is still the most widely used diluent in tablet formulation. Lactose is an excipient that has no reaction with most drugs, whether it is used in the hydrous or anhydrous form.

## Slide 16
Anhydrous lactose has the advantage over lactose in that it does not undergo the Maillard reaction, which can lead to browning and discoloration with certain drugs, as noted previously.
The anhydrous form, however, picks up moisture when exposed to elevated humidity. Such tablets may have to be carefully packaged to prevent moisture exposure. When a wet granulation process is employed, the hydrous form of lactose should generally be used.

## Slide 17
Two grades of lactose are commonly available commercially:
60- to 80-mesh (coarse)
80- to 100-mesh (regular) grade.

## Slide 18
In general, lactose formulations show
Good drug release rates.
Their granulations are readily dried.
The tablet disintegration times of lactose tablets are not strongly sensitive to variations in tablet hardness.
Lactose is a low-cost diluent, but it may discolor in the presence of amine drug bases or salts of alkaline compounds.

## Slide 19
Spray dried lactose is one of several diluents now available for direct compression following mixing with the active ingredient, a disintegrant and a lubricant. If this form of lactose is allowed to dry out and the moisture content falls below 3% level, the material loses some of its direct compressional characteristics.

## Slide 20
In addition to its direct compression properties, spray-dried lactose also has good flow characteristics. It can usually be combined with as much as 20 to 25% of active ingredient without losing these advantageous features. Spray-dried lactose is especially prone to darkening in the presence of excess moisture, amines, and other compounds, owing to the presence of a furaldehyde. A neutral or acid lubricant should be used when spray-dried lactose is employed.

## Slide 21
Starch, which may come from corn, wheat or potatoes, is occasionally used as a tablet diluent.
The USP grade of starch, however, has four flow and compression characteristics and possesses a high typical moisture content of between 11 and 14%. Specially dried types of starch that have a standard moisture level of 2 to 4% are available. Use of such starches in wet granulation is wasteful since their moisture levels increase to 6 to 8% following moisture exposure.

## Slide 22
Various directly compressible starches are now available commercially. Sta-Rx 1500 is one such free flowing, directly compressible starch; it may be used as a diluent, binder, and/or disintegrating agent. Since it is self-lubricating, it may be compressed alone, but when combined with as little as 5 to 10% of drug, it typically requires addition of a lubricant, and
possibly a flow promoter such as 0.25% of a colloidal silicone dioxide. Sta-Rx 1500 contains about 10% moisture and is reportedly prone to softening when combined with excessive amounts (more than 0.5% of magnesium stearate.

## Slide 23
Two hydrolyzed starches are Emdex and Celutab, which are basically 90 to 92% dextrose and about 3 to 5% maltose. They are free-flowing and directly compressible. These materials may be used in place of mannitol in chewable tablets because of their sweetness and smooth feeling in the mouth. These materials contain about 8 to 10% moisture and may increase in hardness after compression.

## Slide 24
Dextrose It is available in two forms: as a hydrate, and in anhydrous form for when low moisture contents are required. Dextrose is sometimes combined in formulation to replace some of the spray-dried lactose, which may reduce the tendency of the resulting tablets to darken.

## Slide 25
Mannitol is perhaps the most expensive sugar used as a tablet diluent, but because of its negative heat of solution, its slow solubility, and its pleasant feeling in the mouth, it is widely used in chewable tablets. It is relatively non hygroscopic and can be used in vitamin formulation, in which moisture sensitivity may be a problem.
Mannitol formulations typically have poor flow characteristics and usually require fairly high lubricant levels.

## Slide 26
Sorbitol is an optical isomer of mannitol and is sometimes combined in mannitol formulations to reduce diluent cost; however, sorbitol is hygroscopic at humidities above 65%. Both of these sugars have a low caloric content and are noncariogenic.

## Slide 27
Microcrystalline cellulose, often referred to by the tradename Avicel, is a direct compression material. Two tablet grades exist: PH 101 (powder) and PH 102 (granules). The flow properties of the material are generally good, and the direct compression characteristics are excellent. This is a somewhat unique diluent in that while producing cohesive compacts, the material also acts as a disintegrating agent. It is, however, a relatively expensive material when used as a diluent in high concentration and is thus typically combined with other materials.

## Slide 28
2. Binders and Adhesives
These materials are added either dry or in liquid form during wet granulation to form granules or to promote cohesive compacts for directly compressed tablets.
Acacia and tragacanth are natural gums and are employed in solutions ranging from 10 to 25% concentration, alone or in combination. These materials are much more effective when they are added as solutions in the preparation of granulations than when they are added dry to a direct compression formula.

## Slide 29
These natural gums have the disadvantage of being variable in their composition and performance based on their natural origin, and they are usually fairly heavily contaminated with bacteria. When these materials are used, their wet granulation masses should be quickly dried at a temperature above 37° to reduce microbial proliferation.

## Slide 30
Gelatin is a natural protein and is sometimes used in combination with acacia. It is a more consistent material than the two natural gums, is easier to prepare in solution form, and forms tablets equally as hard as acacia or tragacanth.

## Slide 31
Starch paste is one of the most common granulating agents. It is prepared by dispersing starch into water, which is then heated for some prescribed time. During the heating, the starch undergoes hydrolysis to dextrin and to glucose. A properly made paste is translucent rather than clear (which would indicate virtually complete conversion to glucose) and produces cohesive tablets that readily disintegrate when properly formulated.

## Slide 32
Modified natural polymers, such as the alginates and cellulose derivatives (methylcellulose, hydroxypropyl methyl cellulose, and hydroxypropyl cellulose), are common binders and adhesives. Used dry for direct compression, they have some binder capabilities, while their aqueous solutions have adhesive properties. Hydroxypropyl cellulose may also be used as an alcohol solution to provide an anhydrous adhesive.

## Slide 33
Ethylcellulose may be used only as an alcoholic solution, and it may be expected to retard disintegration and dissolution time of drugs in the resulting tablets when wet granulation is employed. Polyvinylpyrrolidone is a synthetic polymer that may be used as an adhesive in either an aqueous solution or alcohol. It also has some capabilities as a dry binder.

## Slide 34
3. Disintegrants
A disintegrant is added to most tablet formulations to facilitate a breakup or disintegration of the tablet when it contacts water in the gastrointestinal tract. Disintegrants may function by drawing water into the tablet, swelling, and causing the tablet to burst apart. Such tablet fragmentation may be critical to the subsequent dissolution of the drug and to the attainment of satisfactory drug bioavailability.

## Slide 35
Starch USP and various starch derivatives are the most common disintegrating agents. They also have the lowest cost. Starch is typically used in a concentration range of 5 to 20% of tablet weight. Such modified starches as Primogel and Explotab, which are low substituted carboxylmethyl starches, are used in lower concentrations (1 to 8%, with 4% usually reported as optimum). Various pregelatinized starches are also employed as disintegrants, usually in a 5% concentration.

## Slide 36
Clays such as Veegum HV and bentonite have been used as disintegrants at about a 10% level. Such use of these materials is limited unless the tablets are colored, since the clays produce an off-white appearance. The clays are typically less effective as disintegrants than some of the newer modified polymers and starches, which can increase in volume in the presence of water by 200 to 500%.

## Slide 37
Microcrystalline cellulose have disintegrating characteristics, a new material known as Ac-Di-Sol is now available and is effective in low concentration levels. It is an internally cross-linked form of sodium carboxymethylcellulose.
Another cross-linked polymer that is available as a disintegrant is cross-linked polyvinylpyrrolidone.

## Slide 38
4. Lubricants, Antiadherents and Glidants. A material that is primarily described as an anti-adherent is typically also a lubricant, with some glidant properties as well. The differentiation between these terms is as follows:
Lubricants are intended to reduce the friction during tablet ejection between the walls of the tablet and the walls of the die cavity in which the tablet was formed.

## Slide 39
Antiadherents have the purpose of reducing sticking or adhesion of any of the tablet granulation or powder to the faces of the punches or to the die wall.
Glidants are intended to promote flow of the tablet granulation or powder materials by reducing friction between the particles.

## Slide 40
Hydrocarbon oils such as mineral oil have been employed by application to granulation as a fine spray, either directly or in a solvent solution. The problem with using this type of lubricant is the production of oil spots.
Calcium and magnesium stearate are the most common salts employed. Stearic acid is a less effective lubricant than these salts and also has a lower melting point.

## Slide 41
Talc is probably the second most commonly used tablet lubricant, historically. Most talc samples are found to contain trace quantities of iron, and talc should be considered carefully in any formulation containing a drug whose breakdown is catalyzed by the presence of iron.
The higher- molecular-weight PEG and certain polymeric surfactants have been used as water-soluble lubricants.

## Slide 42
These materials are much less effective as lubricants, however, than the materials previously cited. Since lubrication is basically a coating process, the finer the particle size of the lubricant, the more effective the lubricant action is likely to be.

## Slide 43
5. Colors, Flavors and Sweeteners
The use of colors and dyes in tablet making has served three purposes
Disguising of off-color drugs.
Product identification.
Production of a more elegant product.

## Slide 44
Two forms of color have typically been used in tablet preparation. These are the FD&C and D&C dyes-which are applied as solutions, typically in the granulating agent.
Lakes are dyes that have been absorbed on a hydrous oxide
and usually are employed as dry powders for coloring.

## Slide 45
When using water-soluble dyes, pastel shades usually show the least mottling from uneven distribution in the final tablet.
When wet granulation is employed, care should be taken to prevent color migration during drying.
In any colored tablet, the formulation should be checked for resistance to color changes on exposure to light.

## Slide 46
Flavors are usually limited to chewable tablets or other tablets intended to dissolve in the mouth.
Flavors that are water-soluble have found little acceptance in tablet making because of their poor stability.
Flavor oils are added to tablet granulations in solvents, are dispersed on clays and other absorbents, or are emulsified in aqueous granulating agents.
The maximum amount of oil that can be added to a granulation without influencing its tabletting characteristics is 0.5 to 0.75%.

## Slide 47
The use of sweeteners is primarily limited to chewable
Mannitol is reportedly about 72% as sweet as sucrose.
Saccharin was the only artificial sweetener available and it is about 500 times sweeter than sucrose.
Its major disadvantages are that it has a bitter aftertaste and has been reported to be carcinogenic.
A new artificial sweetener that is expected to largely replace saccharin is aspartame.
The primary disadvantage of aspartame is its lack of stability in the presence of moisture. When aspartame is used in a formulation, e.g., a chewable tablet with hygroscopic components, it will be necessary to determine its stability under conditions in which the product can adsorb atmospheric moisture.

## Slide 48: Tablet Compression Operation

## Slide 49: Tablet Compression Machines Tablets are made by compressing a formulation containing a drug or drugs with excipients on stamping machines called presses.

## Slide 50: Tablet compression machines or tablet presses are designed with the following basic components: 1. Hopper(s) for holding and feeding granulation to be compressed. 2. Dies that define the size and shape of the tablet. 3. Punches for compressing the granulation within the dies. 4. Cam tracks for guiding the movement of the punches. 5. A feeding mechanism for moving granulation from the hopper into the dies.

## Slide 51: Basically, materials intended for compaction into a tablet must possess two characteristics; 1. Fluidity 2. Compressibility

## Slide 52: Good flow properties are essential for the transport of the material through the hopper, into and through the feed frame, and into the dies. Tablet materials should therefore be in a physical form that flows smoothly and uniformly.

## Slide 53: The ideal physical form for this purpose is spheres, since these offer minimum contact surfaces between themselves and with the walls of the machine parts. Unfortunately, most materials do not easily form spheres; however, shapes that approach spheres improve flowability.

## Slide 54: Therefore granulation is the pharmaceutical process that attempts to improve the flow of powdered materials by forming spherelike or regularly shaped aggregates called granules.

## Slide 55: Tablets Manufacturing Methods 1. Direct Compression 2. Granulation . Compression Granulation (Slugging and Roller Compaction). . Wet Granulation.